## Slide 1: P1906.1 Molecular Motor Extension
Stephen F Bush
Thursday, January 29, 2015

## Slide 2: IEEE 1906 NS-3 REFERENCE MODEL
    Exercises definitions, framework, metrics, and use-cases
    Provides base for higher-level nanoscale communication protocols, applications, and standards
    Entertain motion to adopt molecular motor extension into standards repository

## Slide 3: NS-3: THE BIG PICTURE
1906 Framework
1906 Message Carrier
ns-3
EM model
Diffusion model
Motor
model
Nanoscale Network Protocol Layers
Nanoscale Network Applications
Nanoscale Network Systems Scalability and Performance Tests
1906 Message
1906 Motion
1906 Field
1906 Perturbation
1906 Specificity
1906 Medium

## Slide 4: Reference Code Cheat Sheet
Notes on next page

## Slide 5: Reference Code Cheat Sheet

## Slide 6: MOLECULAR MOTOR EXTENSION
  Implements another use-case for the reference model
  Briefly summarize the component class enhancements
  See ../html/classns3_1_1_p1906_m_o_l___microtubules_field.html

## Slide 7: MOLECULAR MOTOR TO 1906 MAP
P1906.1 Component | Molecular Motor
Message Carrier | Molecular Motor + cargo
Motion/Flow/Thrust Potential | Walking + directed diffusion
Field | Microtubule polarity and connectivity
Perturbation | Change in number and types of molecules inside the cargo
Specificity | Receptor sensitivity to cargo
Message Carrier | Molecular Motor + cargo
Motion/Flow/Thrust Potential | Walking + directed diffusion
Field | Microtubule polarity and connectivity
Perturbation | Change in number and types of molecules inside the cargo
Specificity | Receptor sensitivity to cargo
Message Carrier | Molecular Motor + cargo
Stephen F Bush (bushsf@research.ge.com)

## Slide 8: GOALS
Extend IEEE 1906 Field component to enable nanoscale structural modeling
Simple cytoskeletal modeling as an infrastructure for nanoscale communication
Explore entropy of microtubule structure
Explore motor propagation delay to infer information about the structure
Stephen F Bush (bushsf@research.ge.com)

## Slide 9: EXPLORING STRUCTURAL ENTROPY AND MOTOR LATENCY
Can structural entropy be used to characterize channel?
Use graph spectra to estimate propagation delay (Field)
Persistence length as mathematical field
  Persistence length is precisely the expected change in the tangent field lines with distance from one another.
  Tangent lines are the direction of the motor(s) [field lines]
  Orientation is critical for high persistence length
Stephen F Bush (bushsf@research.ge.com)

## Slide 10: RANDOM WALK WITHIN A MATHEMATICAL FIELD
Unbound time: random walk (implemented)
Bound time: follows tangents defined by microtubules (field lines) (almost completed)
How long if no field (pure random walk)? (implemented)
How long if field added (correlated tangents)? (almost completed)
Stephen F Bush (bushsf@research.ge.com)

## Slide 11: 3D TUBE STRUCTURES VS PERSISTENCE LENGTH (1906 FIELD)
Microtubules (tpfig.png)
Stephen F Bush (bushsf@research.ge.com)
HIGH -> LOW
void ns3::P1906MOL_MicrotubulesField::genTubes

## Slide 12: 3D TUBES & INTERSECTION POINTS (1906 FIELD)
Tubes with intersection points laid on top (tubeIntersectionfig.png)
Stephen F Bush (bushsf@research.ge.com)
Points where tubes overlap (pointfig.png)
ns3::P1906MOL_ExtendedField::getOverlap3D

## Slide 13: 3D BROWNIAN MOTION AND TUBE WALK (1906 MOTION)
Brownian motion (motionfig.png)
Bound to Tube (tubeMotionfig.png)
Stephen F Bush (bushsf@research.ge.com)
ns3::P1906MOL_ExtendedMotion::brownianMotion
ns3::P1906MOL_ExtendedMotion::motorWalk

## Slide 14: 3D MOTION ALONG TUBE (1906 MOTION)
Motor motion (red dashed line)
Stephen F Bush (bushsf@research.ge.com)
ns3::P1906MOL_ExtendedMotion::motorWalk

## Slide 15: VECTOR FIELD RECONSTRUCTION (1906 FIELD)
Tangent points along the microtubule structure (vectorField.dat)
Stephen F Bush (bushsf@research.ge.com)
ns3::P1906MOL_ExtendedField::tubes2VectorField

## Slide 16: Message Carrier Flux Meter (P1906MOL_VolSurface)
  Metric: Active Network Programmability
Surface object measures flow through its surface

## Slide 17: INTEGRATION WITH NS-3
Implement microtubules are ns-3 Nodes
  Nodes move as the microtubule network dynamically changes
Ns-3 node mobility
  http://www.nsnam.org/docs/models/html/mobility.html
Matrix math using GNU Scientific Library w/ns-3
  http://www.gnu.org/software/gsl/manual/html_node/Eigenvalue-and-Eigenvector-Examples.html#Eigenvalue-and-Eigenvector-Examples
Stephen F Bush (bushsf@research.ge.com)

## Slide 18: NEXT STEPS (COMMENTS WELCOME)
See
mol-example.cc
_RUN_MOL_CHANNEL_CAPACITY_.sh
Notice that nodeDistance can be passed
./waf --run "scratch/mol-example --nodeDistance=${nodeDistance}“
Perhaps nodePosition could be passed
For Mobility, see
mobility.SetMobilityModel("ns3::ConstantPositionMobilityModel");
The question is how best to integrate and leverage ns-3 capabilities
Stephen F Bush (bushsf@research.ge.com)

## Slide 19: SVN UPDATE INFORMATION
Motor / Microtubule Extensions:
https://code.google.com/p/ieee-p1906-1-reference-code/source/browse/#svn%2Ftrunk%2Fp1906%2Fextensions
Example:
https://code.google.com/p/ieee-p1906-1-reference-code/source/browse/trunk/p1906/examples/microtubules-example.cc
Stephen F Bush (bushsf@research.ge.com)

## Slide 20: INSTALLATION
Make sure GSL is installed
Make sure GSL is enabled in ns-3 using configure
Issue: waf
Move microtubules-example.cc to scratch
Issue: ./waf --run microtubules-example.cc
  Tests will be run and the results output to standard out
  *.mma and *.dat files will be created to imported into Mathematica and MATLAB
Stephen F Bush (bushsf@research.ge.com)

## Slide 21: COMPONENTS/ENTITIES INTERACTION
Stephen F Bush
Stephen F Bush (bushsf@research.ge.com)

## Slide 22: 1906.1 REFERENCE CODE DIAGRAM
Stephen F Bush (bushsf@research.ge.com)

## Slide 23
1906 Framework
1906 Message Carrier
ns-3
EM model
Diffusion model
Motor
model
Nanoscale Network Protocol Layers
Nanoscale Network Applications
Nanoscale Network Systems Scalability and Performance Tests
1906 Message
1906 Motion
1906 Field
1906 Perturbation
1906 Specificity
1906 Medium

## Slide 24: Step 1: Basic Model
Receiver
Transmitter
Noise
Message
Signal
Received
Signal
Message

## Slide 25: Step 2: Small-scale Signal (Perturbation)
1906 Motion
Perturbation of the Medium is much broader than electromagnetic waves
Receiver
Transmitter
Noise
1906 Perturbation

## Slide 26: Step 3: Transporting the Message (Message Carrier)
Receiver
Transmitter
Noise
1906 Message Carrier
1906 Message
1906 Perturbation
1906 Message Carrier
1906 Message
Message Carrier…

## Slide 27: Step 4: Reception (Specificity)
Receiver
Transmitter
Noise
1906 Message Carrier
1906 Message
1906 Perturbation
1906 Specificity
1906 Message Carrier
1906 Message
Specificity…

## Slide 28: Step 5: Motility (Motion)
1906 Motion
Receiver
Transmitter
Noise
1906 Message Carrier
1906 Message
1906 Perturbation
1906 Specificity
1906 Message Carrier
1906 Message
Motion…

## Slide 29: Step 6: Organized Flow (Field)
1906 Motion
Receiver
Transmitter
Noise
1906 Message Carrier
1906 Message
1906 Field
1906 Perturbation
1906 Specificity
1906 Message Carrier
1906 Message
Field…